Comparing resistance and power requirements for Christini AWD bicycle

Lee McCormack • Dec.  3, 2004

Calculations derived from spreadsheet by John Snyder, JCSnyder.studio@worldnet.att.net

Download it here:

http://www.leelikesbikes.com/Stories/112104/BikeForcePower.xls

Rider weight: 180 pounds

Bike weight: 30 pounds

Wheel weight (XC wheels with freeride tires and normal tubes): 8.8 pounds

Rolling resistance coefficient RWD: 0.014 From http://www.me.psu.edu/lamancusa/ProdDiss/Bicycle/bikecalc.htm which got it from "Science of Cycling", E.R. Burke,

Rolling resistance coefficient AWD (+33% per my testing): 0.0182

Aerodynamic drag coefficient: 0.79 for upright position from http://www.damonrinard.com/aero/measuring.htm

Wind speed: 0

Mechanical efficiency: 95 percent. Every bike loses energy in its chain. A perfectly dialed bike still bleeds 5 percent of its energy.

Air temp: 20°C, 68° Fahrenheit

Acceleration rate: moderate rate of 0.8 m/s/s taken from traffic study, www.enhancements.org/trb/1578-16.pdf . Hard rate of 2.0m/s/s roughly doubles that

Figures show the power required in watts

| Scenario | Rolling | Aerodynamic | Slope | Inertia | Efficiency | Total | Change |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 10 mph flat |  |  |  |  |  |  |  |
| RWD | 59 | 44 |  |  | 5 | 108 |  |
| AWD | 77 | 44 |  |  | 6 | 126 | +16.7% |
| 20mph flat |  |  |  |  |  |  |  |
| RWD | 118 | 348 |  |  | 25 | 490 |  |
| AWD | 153 | 348 |  |  | 26 | 528 | +7.8% |
| 10% grade 10mph |  |  |  |  |  |  |  |
| RWD | 59 | 44 | 419 |  | 27 | 549 |  |
| AWD | 76 | 44 | 419 |  | 28 | 567 | +3.3% |
| 20% grade 10mph |  |  |  |  |  |  |  |
| RWD | 58 | 44 | 826 |  | 49 | 976 |  |
| AWD | 75 | 44 | 826 |  | 50 | 995 | +1.9% |
| Hard accel2m/s 5-15mph |  |  |  |  |  |  |  |
| RWD | 59 | 44 |  | 875 | 51 | 1029 |  |
| AWD | 77 | 44 |  | 875 | 52 | 1048 | +1.8% |
| Insane accel4m/s 5-15mph |  |  |  |  |  |  |  |
| RWD | 59 | 44 |  | 1772 | 99 | 1984 |  |
| AWD | 77 | 44 |  | 1772 | 100 | 2003 | +1.0% |